## Slide 1: K. RAMAKRISHNAN COLLEGE OF ENGINEERING
DEPARTMENT OF ECE
SMART PADDY LEAF DISEASE DETECTION WITH ENVIRONMENTAL PARAMATERS FERTILIZER RECOMMENDATION
TEAM MEMBERS:
1) VIJAYABHARATH A - 8115U21EC184 2) SAKTHISIDHARTHAN S - 8115U21EC144 3) SAKTHISARATHI - 8115U21EC145
GUIDED BY :Mrs.KAMALITTA /ASSISTANT HOD

## Slide 2: OBJECTIVES
The objective of the Smart Paddy Leaf Disease Detection with Environmental Parameters & Fertilizer Recommendation system is to enhance crop health and productivity by leveraging artificial intelligence and IoT-based environmental monitoring.
Primary Objective- Detect the disease with fertilizer recommendation in paddy crop.
Secondary Objective – Help the farmers to recommend fertilizer for the best environmental paramaters.

## Slide 3: ABSTRACT
AI-Based Disease Detection
The system uses AI, specifically Vision Transformers with Gaussian Feature Extraction, to detect diseases in paddy leaves.
IoT-Based Environmental Monitoring
IoT sensors collect real-time environmental data to help in better crop management.
Smart Fertilizer Recommendation
Based on detected diseases and soil conditions, the system suggests optimal fertilizers to enhance yield while reducing excessive usage.
Precision & Sustainable Farming
The solution bridges traditional farming with modern AI-driven decision-making, ensuring minimal crop loss and improved efficiency.

## Slide 4: INTRODUCTION
AI-Powered Disease Detection – The system uses Vision Transformers and deep learning to accurately identify paddy leaf diseases.
Real-Time Environmental Monitoring – IoT sensors track soil moisture, temperature, and humidity to help farmers make better decisions.
Smart Fertilizer Recommendations – AI analyzes crop conditions to suggest the right amount of fertilizer, reducing waste and improving yield.
.

## Slide 5: PROBLEM DESCRIPTION
Slow and Inaccurate Disease Detection – Manual checking of crops takes time, can be wrong, and delays treatment, harming crop health and yield.
Lack of Smart Farming – Without AI and IoT, farmers can't monitor crops in real time or make data-driven decisions, leading to wasted resources and lower productivity.

## Slide 6: LITERATURE SURVEY

## Slide 7
Publisher | Title | Authors | Year | Technique | Advantages | Disadvantages
IEEE | Paddy Leaf Diseases Identification on Infrared Images Based on CNN | Petchiammal A., Briskline Kiruba S., D. Murugan | 2022 | CNN on infrared images | 88.28% accuracy in classifying five paddy diseases | Small dataset (636 images), potential overfitting
IEEE | A Channel Attention-Driven Hybrid CNN Framework for Paddy Leaf Disease Detection | Pandiyaraju V., Shravan V., Abeshek A., Pavan Kumar S., et al. | 2024 | Hybrid CNN with channel attention and Swish ReLU activation | 99.76% F1-score, 99.74% accuracy | Increased complexity due to attention mechanism

## Slide 8
Publisher | Title | Authors | Year | Technique | Advantages | Disadvantages
IEEE | Paddy Doctor: A Visual Image Dataset for Automated Paddy Disease Classification | Petchiammal A., Briskline Kiruba S., Murugan D., Pandarasamy A. | 2022 | CNN and transfer learning on 16,225 annotated images | Large dataset, ResNet34 achieved 97.50% F1-score | Dataset imbalance may affect classification
IEEE | Plant Diseases Recognition Using CNN: A Systematic Review | Andre S. Abade, Paulo A. Ferreira, Flavio de B. Vidal | 2020 | Review of CNN applications in plant disease detection | Overview of trends, highlights gaps | Not specific to paddy diseases, broad scope

## Slide 9
Publisher | Title | Authors | Year | Technique | Advantages | Disadvantages
PubMed | Advancements in Rice Disease Detection Through CNN: A Comprehensive Review | Not specified | 2024 | Review of CNN for rice disease detection | Analyzes datasets and models | No new methodologies, lacks implementation details
IJISA Engineering | Rice Leaf Disease Detection and Remedies Using Deep Learning | Ravindra Gahane, Rajani P. K., et al. | 2024 | CNN for real-time rice leaf disease diagnosis | 98% accuracy, user-friendly web interface | Limited to four specific diseases

## Slide 10: EXISTING ISSUES
Manual disease detection is time-consuming and prone to errors, leading to delayed treatment and crop loss.
Lack of real-time environmental monitoring and data-driven fertilizer recommendations results in inefficient farming practices.
DRAWBACKS
Manual disease detection is time-consuming and error-prone.
Lack of real-time monitoring affects timely disease prevention.

## Slide 11: PROPOSED SYSTEM
AI-Powered Disease Detection – Vision Transformers and deep learning accurately detect paddy leaf diseases, enabling automated and early diagnosis.
Smart Farming with IoT – Real-time environmental monitoring and AI-driven fertilizer recommendations improve decision-making, reduce costs, and promote sustainable farming.

## Slide 12: SYSTEM ARCHITECTUE
Trained data
Identification
Data collection
Image acquisition
Noise filtering
Feature Extraction
Training
Testing

## Slide 13: ADVANTAGE
AI-based disease detection ensures high accuracy and early treatment.
IoT real-time monitoring improves farming efficiency and productivity.
Smart fertilizer recommendations reduce waste and enhance soil health.

## Slide 14: MODULE LIST
Software
Image acquisition
Pre-processing
Feature Extraction
Training
VT classification
Fertilizer recommendation
Hardware
Connection system
Sensor detection
Fertilizer matching
SMS alert

## Slide 15: SOFTWARE REQUIREMENT
SOFTWARE REQUIREMENTS
Front End : Python, Embedded C
IDE : Pycharm Community Edition
platform : windows 10
IOT TOOL : Arduino

## Slide 16: MODULE DESCRIPTION
Software Process:
Image Acquisition: Captures paddy leaf images using IoT-enabled cameras for disease detection.
Pre-processing: Enhances image quality by noise reduction and contrast adjustment for better analysis.
Feature Extraction: Identifies key disease-related patterns using Gaussian Feature Extraction.
Training: Vision Transformers (VT) model is trained with labeled disease data for accurate classification.
VT Classification: Uses AI to classify paddy leaf diseases based on extracted features.
Fertilizer Recommendation: Suggests optimal fertilizers based on disease type and soil conditions.

## Slide 17: MODULE DESCRIPTION
Hardware Process:
Connection System: Integrates IoT devices, cameras, and sensors for real-time data collection.
Sensor Detection: Monitors environmental parameters like soil moisture and temperature.
Fertilizer Matching: Matches detected disease with the best-suited fertilizer for effective treatment.
SMS Alert: Sends disease detection and fertilizer recommendation alerts to farmers via SMS.

## Slide 18: CONCLUSION
1. Accurate Disease Detection – AI with Vision Transformers and Gaussian Feature Extraction helps classify paddy leaf diseases with high accuracy.
2. Smart Monitoring and Alerts – IoT sensors provide real-time environmental data and instant alerts, helping farmers take quick action.
3. Sustainable Farming – The system gives smart fertilizer recommendations, reducing waste, preventing crop loss, and improving overall farm efficiency.

## Slide 19: FUTURE WORK
Better Disease Detection – Improving AI models for more accurate paddy leaf disease identification and treatment suggestions.
Smart Fertilizer Use – Using real-time weather and soil data to give better fertilizer advice and boost crop growth.
Support for More Crops – Expanding the system to detect diseases and give recommendations for different types of crops.

## Slide 20: REFERENCES
Paddy Disease Detection and Classification Using Computer Vision Techniques: A Mobile Application to Detect Paddy Disease, arXiv, 2024.
An Enhancement of CNN Algorithm for Rice Leaf Disease Image Classification in Mobile Applications, arXiv, 2024. Precision Agriculture Technology for Crop Farming, CRC Press, 2016.
An IoT-based Smart Irrigation Management System Using Machine Learning and Open Source Technologies, Computers and Electronics in Agriculture, 2018.
Determining and Predicting Soil Chemistry with a Point-of-Use Sensor Toolkit and Machine Learning Model, bioRxiv, 2020.

## Slide 21: THANK YOU